## Slide 1: Chapter 1
C for Embedded Systems

## Slide 2: Chapter Review
Section 1.1: C Data types for Embedded Systems
Section 1.2: Bit-wise Operations in C

## Slide 3: Sizes of Data Types
three methods to find out the exact sizes of the data types:
Read the compiler manual.
Use pseudo function sizeof().
Use C99 data types.

## Slide 4: Why should I care about which data type to use?
Performance
Overflow
coercion

## Slide 5: Performance
Using 64-bit data type for saving 32-bit variable will cause:
Waste RAM resource
Twice RAM access time
Additional arithmetic instructions

## Slide 6: ANSI C (ISO C89) integer data types and their ranges
Data type | Size | Range Min | Range Max
char | 1 byte | -128 | 127
unsigned char | 1 byte | 0 | 255
short int | 2 bytes | -32,768 | 32,767
unsigned short int | 2 bytes | 0 | 65,535
int | 4 bytes | -2,147,483,648 | 2,147,483,647
unsigned int | 4 bytes | 0 | 4,294,967,295
long | 4 bytes | -2,147,483,648 | 2,147,483,647
unsigned long | 4 bytes | 0 to 4,294,967,295 | 
long long | 8 bytes | -9,223,372,036,854,775,808 | 9,223,372,036,854,775,807
unsigned long long | 8 bytes | 0 | 18,446,744,073,709,551,615

## Slide 7: Overflow
Unlike assembly language programming, high level language programs do not provide indications when overflow occurs and the program just fails silently.
If you use a short int to hold the number of seconds of a day, the second count will overflow from 32,767 to -32,768. Even if your program handles negative second count, the time will jump back to the day before.

## Slide 8: Coercion
If you write a statement with different operand data types for a binary operation, the compiler will convert the smaller data type to the bigger data type. These implicit data type is called coercion.
The compiler may or may not give you warning when coercion occurs.
If the variable is signed and the data sized is increased, the new bits are filled with the sign bit (most significant bit) of the original value.
When you assign a larger data type to a smaller data type variable, the higher order bits will be truncated.

## Slide 9: ISO C99 integer data types and their ranges
Data type | Size | Range Min | Range Max
int8_t | 1 byte | -128 | 127
uint8_t | 1 byte | 0 to | 255
int16_t | 2 bytes | -32,768 | 32,767
uint16_t | 2 bytes | 0 | 65,535
int32_t | 4 bytes | -2,147,483,648 | 2,147,483,647
uint32_t | 4 bytes | 0 | 4,294,967,295
int64_t | 8 bytes | -9,223,372,036,854,775,808 | 9,223,372,036,854,775,807
uint64_t | 8 bytes | 0 | 18,446,744,073,709,551,615

## Slide 10: Bit-wise operators in C
A | B | AND (A & B) | OR (A ¦ B) | EX-OR (A^B) | Invert ~B
0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1 | 0
1 | 0 | 0 | 1 | 1 | 1
1 | 1 | 1 | 1 | 0 | 0

## Slide 11: Setting and Clearing (masking) bits
Anything ORed with a 1 results in a 1; anything ORed with a 0 results in no change.
Anything ANDed with a 1 results in no change; anything ANDed with a 0 results in a zero.
Anything EX-ORed with a 1 results in the complement; anything EX-ORed with a 0 results in no change.

## Slide 12: Testing bit with bit-wise operators in C
When it is necessary to test a given bit to see if it is high or low, the unused bits are masked and then the remaining data is tested.
Example: if (var1 & 0x20)

## Slide 13: Bit-wise shift operation in C
Operation | Symbol | Format of Shift Operation
Shift Right | >> | data >> number of bit-positions to be shifted right
Shift Left | << | data << number of bit-positions to be shifted left

## Slide 14: Compound Operators
Instruction | Its equivalent using compound operators
a = a + 6; | a += 6;
a = a – 23; | a –= 23;
y = y * z; | y *= z;
z = z / 25; | z /= 25;
w = w ¦ 0x20; | w ¦= 0x20;
v = v & mask; | v &= mask;
m = m ^ togBits; | m ^= togBits;

## Slide 15: Bit-wise operations using compound operators
The majority of hardware access level code involves setting a bit or bits in a register, clearing a bit or bits in a register, toggling a bit or bits in a register, and monitoring the status bits. For the first three cases, the compound operators are very suitable.

## Slide 16: Using shift operator to generate mask
One way to ease the generation of the mask is to use the left shift operator. To generate a mask with bit n set to 1, use the expression: 1 << n
If more bits are to be set in the mask, they can be “or” together. To generate a mask with bit n and bit m set to 1, use the expression: (1 << n) | (1 << m)
register |= (1 << 6) | (1 << 1);

## Slide 17: Setting the value in a multi-bit field
register |= 1 << 30; register &= ~(1 << 29); register |= 1 << 28;
register &= ~(7 << 28); register |= 5 << 28;
register = register & ~(7 << 28) | (5 << 28);