## Slide 1: Chapter 2
Atmel ARM I/O Programming

## Slide 2: Arduino Zero using Atmel SAM D21

## Slide 3: Atmel SAM D Microcontroller Block Diagram

## Slide 4: Atmel D20 Xplained Pro development board

## Slide 5: Atmel D21 Xplained Pro development board

## Slide 6: Memory Map of Atmel SAM D2xJ18
 | Memory sizes | Address range
Flash | 256KB | 0x00000000-0x0003FFFF
SRAM | 32KB | 0x20000000-0x20007FFF
I/O | All the peripherals | 0x40000000-0x420053FF

## Slide 7: Memory map for ATSAMD21J18

## Slide 8: Fields Values Description
Field | Description | Some Valid Values
SAM D | Product Family | General Purpose MCU
## | Product Series | • 09 = Cortex-M0+ Basic Feature Set •910 = Cortex-M0+ CPU, Basic Feature Set, TCC, DMA •011 = D10 + USB Device •120 = Cortex-M0+ CPU, Basic Feature Set •021 = D20 + USB Device and Embedded Host, I2S, DMA, TCC, 3.4MHz I2C
P | Pin Count | • C = 14 pins • D = 20/24 pins • E = 32 pins • G = 48 pins • J = 64 pins
FM | Flash Memory | • 13 = 8 KB •K14 = 16 KB •K15 = 32 KB •KB6 = 64 KB • = 64 KB8 KB • KB = 256 KB
A | Marketing Revision | • A = Initial Revision
X | Package Type | • A = TQFP • M = QFN • SS = SOIC
Y | Plating material and temp grade | •lU = -40 — 85°C Matte Sn plating •=N = -40 — 105°C Matte Sn plating
Z | Package carrier | •aT = Tape & Reel •=No character = Tray/Tube (Default)

## Slide 9: Atmel SAM D MCU features

## Slide 10: Atmel SAM MCU portfolio

## Slide 11: ATSAMD21J18 pinout

## Slide 12: Peripheral address map of SAM D21

## Slide 13: The Data and Direction Registers and a Simplified View of an I/O pin

## Slide 14: OUTput Register

## Slide 15: DIRection Register

## Slide 16: APBB Mask register of Power Management

## Slide 17: LED connection to PB30 of the SAMD21 Xplained Pro board

## Slide 18: LED connection to PA14 of the SAMD20 Xplained Pro board

## Slide 19: OUTSET (Output Set) Register

## Slide 20: OUTCLR (Output Clear) Register

## Slide 21: OUTTGL (Output Toggle) Register

## Slide 22: Some GPIO registers
Address (Offset) | Name | Description | Type | Reset Value
0x00 | DIR | Port Data Direction Register | R/W | 0x00000000
0x04 | DIRCLR | Port Data Direction Clear Register | R/W | 0x00000000
0x08 | DIRSET | Port Direction Set Register | R/W | 0x00000000
0x0C | DIRTGL | Port Direction Toggle Register | R/W | 0x00000000
0x10 | OUT | Port Data Output Register | R/W | 0x00000000
0x14 | OUTCLR | Port Output Clear Register | R/W | 0x00000000
0x18 | OUTSET | Data Output Value Set | R/W | 0x00000000
0x1C | OUTTGL | Data Output Value Toggle | R/W | 0x00000000
0x20 | IN | Data Input Value | R | 0x00000000

## Slide 23: User switch connection on SAMD21 Xplained Pro board

## Slide 24: Connecting external switches to the microcontroller

## Slide 25: An input pin configured with pull-up/down enabled

## Slide 26: PINCFG register

## Slide 27: Bit descriptions of PINCFG registers
BIT | Field | Description
6 | DRVSTR | Output Driver Strength Selection 0: Pin drive strength is set to normal drive strength. 1: Pin drive strength is set to stronger drive strength.
2 | PULLEN | Pull Enable 0: Internal pull resistor is disabled, and the input is in a high-impedance configuration. 1: Internal pull resistor is enabled, and the input is driven to a defined logic level in the absence of external input.
1 | INEN | Input Enable 0: Input buffer for the I/O pin is disabled, and the input value will not be sampled. 1: Input buffer for the I/O pin is enabled, and the input value will be sampled when required.
0 | PMUXEN | Peripheral Multiplexer Enable 0: The peripheral multiplexer selection is disabled, and the PORT registers control the direction and output drive value. 1: The peripheral multiplexer selection is enabled, and the selected peripheral controls the direction and output drive value.

## Slide 28: GPIO pin configurations

## Slide 29: Pin multiplexing of alternate functions

## Slide 30: PINCFGn register (notice the PMUXEN bit)

## Slide 31: PMUX Register is used to select alternate pin functions

## Slide 32: PMUX register options

## Slide 33: Atmel SAM D21 Alternative Pin Functions
 |  | A (0) | B (1) |  |  |  |  | C (2) | D (3) | E (4) | F (5) | G (6) | H (7)
I/O Pin | Supply | EIC | REF | ADC | AC | PTC | DAC | SERCOM | SERCOM-ALT | TC/TCC | TCC | COM | AC/GCLK
PA00 | VDDANA | EXTINT[0] |  |  |  |  |  |  | SERCOM1/PAD[0] | TCC2/WO[0] |  |  | 
PA01 | VDDANA | EXTINT[1] |  |  |  |  |  |  | SERCOM1/PAD[1] | TCC2/WO[1] |  |  | 
PA02 | VDDANA | EXTINT[2] |  | AIN[0] |  | Y[0] | VOUT |  |  |  |  |  | 
PA03 | VDDANA | EXTINT[3] | ADC/VREFA DAC/VREFA | AIN[1] |  | Y[1] |  |  |  |  |  |  | 
PA04 | VDDANA | EXTINT[4] | ADC/VREFB | AIN[4] | AIN[0] | Y[2] |  |  | SERCOM0/PAD[0] | TCC0/WO[0] |  |  | 
PA05 | VDDANA | EXTINT[5] |  | AIN[5] | AIN[1] | Y[3] |  |  | SERCOM0/PAD[1] | TCC0/WO[1] |  |  | 
PA06 | VDDANA | EXTINT[6] |  | AIN[6] | AIN[2] | Y[4] |  |  | SERCOM0/PAD[2] | TCC1/WO[0] |  |  | 
PA07 | VDDANA | EXTINT[7] |  | AIN[7] | AIN[3] | Y[5] |  |  | SERCOM0/PAD[3] | TCC1/WO[1] |  | I2S/SD[0] | 
PA08 | VDDIO | NMI |  | AIN[16] |  | X[0] |  | SERCOM0/PAD[0] | SERCOM2/PAD[0] | TCC0/WO[0] | TCC1/WO[2] | I2S/SD[1] | 
PA09 | VDDIO | EXTINT[9] |  | AIN[17] |  | X[1] |  | SERCOM0/PAD[1] | SERCOM2/PAD[1] | TCC0/WO[1] | TCC1/WO[3] | I2S/MCK[0] | 
PA10 | VDDIO | EXTINT[10] |  | AIN[18] |  | X[2] |  | SERCOM0/PAD[2] | SERCOM2/PAD[2] | TCC1/WO[0] | TCC0/WO[2] | I2S/SCK[0] | GCLK_IO[4]
PA11 | VDDIO | EXTINT[11] |  | AIN[19] |  | X[3] |  | SERCOM0/PAD[3] | SERCOM2/PAD[3] | TCC1/WO[1] | TCC0/WO[3] | I2S/FS[0] | GCLK_IO[5]
PA12 | VDDIO | EXTINT[12] |  |  |  |  |  | SERCOM2/PAD[0] | SERCOM4/PAD[0] | TCC2/WO[0] | TCC0/WO[6] |  | AC/CMP[0]
PA13 | VDDIO | EXTINT[13] |  |  |  |  |  | SERCOM2/PAD[1] | SERCOM4/PAD[1] | TCC2/WO[1] | TCC0/WO[7] |  | AC/CMP[1]
PA14 | VDDIO | EXTINT[14] |  |  |  |  |  | SERCOM2/PAD[2] | SERCOM4/PAD[2] | TC3/WO[0] | TCC0/WO[4] |  | GCLK_IO[0]
PA15 | VDDIO | EXTINT[15] |  |  |  |  |  | SERCOM2/PAD[3] | SERCOM4/PAD[3] | TC3/WO[1] | TCC0/WO[5] |  | GCLK_IO[1]
PA16 | VDDIO | EXTINT[0] |  |  |  | X[4] |  | SERCOM1/PAD[0] | SERCOM3/PAD[0] | TCC2/WO[0] | TCC0/WO[6] |  | GCLK_IO[2]
PA17 | VDDIO | EXTINT[1] |  |  |  | X[5] |  | SERCOM1/PAD[1] | SERCOM3/PAD[1] | TCC2/WO[1] | TCC0/WO[7] |  | GCLK_IO[3]
PA18 | VDDIO | EXTINT[2] |  |  |  | X[6] |  | SERCOM1/PAD[2] | SERCOM3/PAD[2] | TC3/WO[0] | TCC0/WO[2] |  | AC/CMP[0]
PA19 | VDDIO | EXTINT[3] |  |  |  | X[7] |  | SERCOM1/PAD[3] | SERCOM3/PAD[3] | TC3/WO[1] | TCC0/WO[3] | I2S/SD[0] | AC/CMP[1]
PA20 | VDDIO | EXTINT[4] |  |  |  | X[8] |  | SERCOM5/PAD[2] | SERCOM3/PAD[2] | TC7/WO[0] | TCC0/WO[6] | I2S/SCK[0] | GCLK_IO[4]
PA21 | VDDIO | EXTINT[5] |  |  |  | X[9] |  | SERCOM5/PAD[3] | SERCOM3/PAD[3] | TC7/WO[1] | TCC0/WO[7] | I2S/FS[0] | GCLK_IO[5]
PA22 | VDDIO | EXTINT[6] |  |  |  | X[10] |  | SERCOM3/PAD[0] | SERCOM5/PAD[0] | TC4/WO[0] | TCC0/WO[4] |  | GCLK_IO[6]
PA23 | VDDIO | EXTINT[7] |  |  |  | X[11] |  | SERCOM3/PAD[1] | SERCOM5/PAD[1] | TC4/WO[1] | TCC0/WO[5] | USB/SOF 1kHz | GCLK_IO[7]

## Slide 34: Atmel SAM D21 Alternative Pin Functions
PA24 | VDDIO | EXTINT[12] |  |  |  |  |  | SERCOM3/PAD[2] | SERCOM5/PAD[2] | TC5/WO[0] | TCC1/WO[2] | USB/DM | 
PA25 | VDDIO | EXTINT[13] |  |  |  |  |  | SERCOM3/PAD[3] | SERCOM5/PAD[3] | TC5/WO[1] | TCC1/WO[3] | USB/DP | 
PA27 | VDDIO | EXTINT[15] |  |  |  |  |  |  |  |  |  |  | GCLK_IO[0]
PA28 | VDDIO | EXTINT[8] |  |  |  |  |  |  |  |  |  |  | GCLK_IO[0]
PA30 | VDDIO | EXTINT[10] |  |  |  |  |  |  | SERCOM1/PAD[2] | TCC1/WO[0] |  | SWCLK | GCLK_IO[0]
PA31 | VDDIO | EXTINT[11] |  |  |  |  |  |  | SERCOM1/PAD[3] | TCC1/WO[1] |  | SWDIO(4) | 
PB00 | VDDANA | EXTINT[0] |  | AIN[8] |  | Y[6] |  |  | SERCOM5/PAD[2] | TC7/WO[0] |  |  | 
PB01 | VDDANA | EXTINT[1] |  | AIN[9] |  | Y[7] |  |  | SERCOM5/PAD[3] | TC7/WO[1] |  |  | 
PB02 | VDDANA | EXTINT[2] |  | AIN[10] |  | Y[8] |  |  | SERCOM5/PAD[0] | TC6/WO[0] |  |  | 
PB03 | VDDANA | EXTINT[3] |  | AIN[11] |  | Y[9] |  |  | SERCOM5/PAD[1] | TC6/WO[1] |  |  | 
PB04 | VDDANA | EXTINT[4] |  | AIN[12] |  | Y[10] |  |  |  |  |  |  | 
PB05 | VDDANA | EXTINT[5] |  | AIN[13] |  | Y[11] |  |  |  |  |  |  | 
PB06 | VDDANA | EXTINT[6] |  | AIN[14] |  | Y[12] |  |  |  |  |  |  | 
PB07 | VDDANA | EXTINT[7] |  | AIN[15] |  | Y[13] |  |  |  |  |  |  | 
PB08 | VDDANA | EXTINT[8] |  | AIN[2] |  | Y[14] |  |  | SERCOM4/PAD[0] | TC4/WO[0] |  |  | 
PB09 | VDDANA | EXTINT[9] |  | AIN[3] |  | Y[15] |  |  | SERCOM4/PAD[1] | TC4/WO[1] |  |  | 
PB10 | VDDIO | EXTINT[10] |  |  |  |  |  |  | SERCOM4/PAD[2] | TC5/WO[0] | TCC0/WO[4] | I2S/MCK[1] | GCLK_IO[4]
PB11 | VDDIO | EXTINT[11] |  |  |  |  |  |  | SERCOM4/PAD[3] | TC5/WO[1] | TCC0/WO[5] | I2S/SCK[1] | GCLK_IO[5]
PB12 | VDDIO | EXTINT[12] |  |  |  | X[12] |  | SERCOM4/PAD[0] |  | TC4/WO[0] | TCC0/WO[6] | I2S/FS[1] | GCLK_IO[6]
PB13 | VDDIO | EXTINT[13] |  |  |  | X[13] |  | SERCOM4/PAD[1] |  | TC4/WO[1] | TCC0/WO[7] |  | GCLK_IO[7]
PB14 | VDDIO | EXTINT[14] |  |  |  | X[14] |  | SERCOM4/PAD[2] |  | TC5/WO[0] |  |  | GCLK_IO[0]
PB15 | VDDIO | EXTINT[15] |  |  |  | X[15] |  | SERCOM4/PAD[3] |  | TC5/WO[1] |  |  | GCLK_IO[1]
PB16 | VDDIO | EXTINT[0] |  |  |  |  |  | SERCOM5/PAD[0] |  | TC6/WO[0] | TCC0/WO[4] | I2S/SD[1] | GCLK_IO[2]
PB17 | VDDIO | EXTINT[1] |  |  |  |  |  | SERCOM5/PAD[1] |  | TC6/WO[1] | TCC0/WO[5] | I2S/MCK[0] | GCLK_IO[3]
PB22 | VDDIO | EXTINT[6] |  |  |  |  |  |  | SERCOM5/PAD[2] | TC7/WO[0] |  |  | GCLK_IO[0]
PB23 | VDDIO | EXTINT[7] |  |  |  |  |  |  | SERCOM5/PAD[3] | TC7/WO[1] |  |  | GCLK_IO[1]
PB30 | VDDIO | EXTINT[14] |  |  |  |  |  |  | SERCOM5/PAD[0] | TCC0/WO[0] | TCC1/WO[2] |  | 
PB31 | VDDIO | EXTINT[15] |  |  |  |  |  |  | SERCOM5/PAD[1] | TCC0/WO[1] | TCC1/WO[3] |  | 

## Slide 35: Seven-segment Display

## Slide 36: Assignments of port pins to each segments of a 7-seg LED
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
. | g | F | e | d | c | b | a

## Slide 37: Segment patterns for the 10 decimal digits for a common cathode 7-seg LED
Num | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | Hex value
 | . | g | f | e | d | c | b | a | 
0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0x3F
1 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0x06
2 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 0x5B
3 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 0x4F
4 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0x66
5 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 0x6D
6 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0x7D
7 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0x07
8 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0x7F
9 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0x6F

## Slide 38: Connections between microcontroller and a two-digit 7-segment LED

## Slide 39: Connections between microcontroller and 7-segment LED with drivers