## Slide 1: Chapter 4
UART Serial Port Programming

## Slide 2: Serial vs. Parallel Data Transfer

## Slide 3: Parallel In Serial Out

## Slide 4: Serial In Parallel Out

## Slide 5: Simplex, Half-, and Full-Duplex Transfers

## Slide 6: Framing ASCII "A" (0x41)

## Slide 7: MAX232

## Slide 8: MAX233

## Slide 9: RS232 Pins
Pin | Description
1 | Data carrier detect (DCD)
2 | Received data (RxD)
3 | Transmitted data (TxD)
4 | Data terminal ready (DTR)
5 | Signal ground (GND)
6 | Data set ready (DSR)
7 | Request to send (RTS)
8 | Clear to send (CTS)
9 | Ring indicator (RI)

## Slide 10: 9-Pin Male Connector

## Slide 11: DTE-DCE and DTE-DTE Connections

## Slide 12: Null Modem Connection with Flow Control Signals

## Slide 13: Atmel SAMD21 Xplained Pro board

## Slide 14: Embedded Debug USB port

## Slide 15: Partial list of SERCOMx Registers and their addresses
Register Name | Register Function | Register Address Offset (Hex)
CTRLA | Control A | 0000
CTRLB | Control B | 0004
BAUD | Baud Rate | 000C
INTFLAG | Interrupt Flag | 0018
STATUS | Status 1 | 001A
DATA | DATA | 0028

## Slide 16: A Simplified Block Diagram of UART

## Slide 17: APBC MASK Resgister bit assignments

## Slide 18: APBC MASK Resgister bit assignments

## Slide 19: APBC Clock Select Resgister bit assignment

## Slide 20: Generic Clock Control Resgister bit assignment

## Slide 21: Clock division for SERCOM in USART mode

## Slide 22: BAUD Register (as a 16-bit integer in arithmetic mode)

## Slide 23: BAUD register with fraction in fraction mode

## Slide 24: CTLA Register bits for sample rate factor

## Slide 25: Sample rate options in CTRLA register
SAMPR[2:0] | Descriptions
0x0 | 16x over-sampling using arithmetic baud rate generation.
0x1 | 16x over-sampling using fractional baud rate generation.
0x2 | 8x over-sampling using arithmetic baud rate generation.
0x3 | 8x over-sampling using fractional baud rate generation.
0x4 | 3x over-sampling using arithmetic baud rate generation.
0x5-0x7 | Reserved

## Slide 26: BAUD Register Values for Some Baud Rates using S=16 and clock of 48 MHz
Baud rate | BAUD (in decimal) | BAUD (in hex)
4,800 | 65,431 | 0xFF97
9,600 | 65,326 | 0xFF2E
19,200 | 65,117 | 0xFE5D
38,400 | 64,697 | 0xFCB9
115,200 | 63,019 | 0xF62B

## Slide 27: UART Control A (CTRLA) register

## Slide 28: UART Control B (CTRLB) register

## Slide 29: UART Data (DATA) register

## Slide 30: UART Interrupt Flag Register (INTFLAG)

## Slide 31: UART Interrupt Flag register (INTFLAG)
Field | Bit | Description
ERROR | 7 | Error This flag is cleared by writing a one to it. This bit is set when any error is detected. Errors that will set this flag have corresponding status flags in the STATUS register. Errors that will set this flag are COLL, ISF, BUFOVF, FERR, and PERR. 0 = No effect 1 = Clear the flag
 | 6 | Reserved
RXBRK | 5 | Receive Break This flag is cleared by writing a one to it. This flag is set when auto-baud is enabled (CTRLA.FORM) and a break character is received. 0 = No effect 1 = Clear the flag
CTSIC | 4 | Clear to Send Input Change This flag is cleared by writing a one to it. This flag is set when a change is detected on the CTS pin. 0 = No effect 1 = Clear the flag

## Slide 32: UART Interrupt Flag register (INTFLAG)
Field | Bit | Description
RXS | 3 | Receive Start This flag is cleared by writing a one to it. This flag is set when a start condition is detected on the RxD line and start-of-frame detection is enabled (CTRLB.SFDE is one). 0 = No effect 1 = Clear the Receive Start interrupt flag
RXC | 2 | Receive Complete This flag is cleared by reading the Data register (DATA) or by disabling the receiver. This flag is set when there are unread data in DATA 0 = No effect 1 = No effect
TXC | 1 | Transmit Complete This flag is cleared by writing a one to it or by writing new data to DATA. This flag is set when the entire frame in the transmit shift register has been shifted out and there are no new data in DATA. 0 = No effect 1 = Clear the flag
DRE | 0 | Data Register Empty This flag is cleared by writing new data to DATA. This flag is set when DATA is empty and ready to be written. 0 = No effect 1 = No effect

## Slide 33: UART Status Register (STATUS)

## Slide 34: PINCFGn register (notice the PMUXEN bit)

## Slide 35: PMUX register for choosing peripheral functions

## Slide 36: SAMD2x Signals Used for UART (See CTRLA register)
TXPO[1:0] | PAD | RXPO[1:0] | PAD
0x0 | PAD[0] | 0x0 | PAD[0]
0x1 | PAD[2] | 0x1 | PAD[1]
0x2 | PAD[0] | 0x2 | PAD[2]
0x3 | Reserved | 0x3 | PAD[3]

## Slide 37: Pin Multiplexing SAMD21J
 |  | A (0) | B (1) |  |  |  |  | C (2) | D (3) | E (4) | F (5) | G (6) | H (7)
I/O Pin | Supply | EIC | REF | ADC | AC | PTC | DAC | SERCOM | SERCOM-ALT | TC/TCC | TCC | COM | AC/GCLK
PA00 | VDDANA | EXTINT[0] |  |  |  |  |  |  | SERCOM1/PAD[0] | TCC2/WO[0] |  |  | 
PA01 | VDDANA | EXTINT[1] |  |  |  |  |  |  | SERCOM1/PAD[1] | TCC2/WO[1] |  |  | 
PA02 | VDDANA | EXTINT[2] |  | AIN[0] |  | Y[0] | VOUT |  |  |  |  |  | 
PA03 | VDDANA | EXTINT[3] | ADC/VREFA DAC/VREFA | AIN[1] |  | Y[1] |  |  |  |  |  |  | 
PA04 | VDDANA | EXTINT[4] | ADC/VREFB | AIN[4] | AIN[0] | Y[2] |  |  | SERCOM0/PAD[0] | TCC0/WO[0] |  |  | 
PA05 | VDDANA | EXTINT[5] |  | AIN[5] | AIN[1] | Y[3] |  |  | SERCOM0/PAD[1] | TCC0/WO[1] |  |  | 
PA06 | VDDANA | EXTINT[6] |  | AIN[6] | AIN[2] | Y[4] |  |  | SERCOM0/PAD[2] | TCC1/WO[0] |  |  | 
PA07 | VDDANA | EXTINT[7] |  | AIN[7] | AIN[3] | Y[5] |  |  | SERCOM0/PAD[3] | TCC1/WO[1] |  | I2S/SD[0] | 
PA08 | VDDIO | NMI |  | AIN[16] |  | X[0] |  | SERCOM0/PAD[0] | SERCOM2/PAD[0] | TCC0/WO[0] | TCC1/WO[2] | I2S/SD[1] | 
PA09 | VDDIO | EXTINT[9] |  | AIN[17] |  | X[1] |  | SERCOM0/PAD[1] | SERCOM2/PAD[1] | TCC0/WO[1] | TCC1/WO[3] | I2S/MCK[0] | 
PA10 | VDDIO | EXTINT[10] |  | AIN[18] |  | X[2] |  | SERCOM0/PAD[2] | SERCOM2/PAD[2] | TCC1/WO[0] | TCC0/WO[2] | I2S/SCK[0] | GCLK_IO[4]
PA11 | VDDIO | EXTINT[11] |  | AIN[19] |  | X[3] |  | SERCOM0/PAD[3] | SERCOM2/PAD[3] | TCC1/WO[1] | TCC0/WO[3] | I2S/FS[0] | GCLK_IO[5]
PA12 | VDDIO | EXTINT[12] |  |  |  |  |  | SERCOM2/PAD[0] | SERCOM4/PAD[0] | TCC2/WO[0] | TCC0/WO[6] |  | AC/CMP[0]
PA13 | VDDIO | EXTINT[13] |  |  |  |  |  | SERCOM2/PAD[1] | SERCOM4/PAD[1] | TCC2/WO[1] | TCC0/WO[7] |  | AC/CMP[1]
PA14 | VDDIO | EXTINT[14] |  |  |  |  |  | SERCOM2/PAD[2] | SERCOM4/PAD[2] | TC3/WO[0] | TCC0/WO[4] |  | GCLK_IO[0]
PA15 | VDDIO | EXTINT[15] |  |  |  |  |  | SERCOM2/PAD[3] | SERCOM4/PAD[3] | TC3/WO[1] | TCC0/WO[5] |  | GCLK_IO[1]
PA16 | VDDIO | EXTINT[0] |  |  |  | X[4] |  | SERCOM1/PAD[0] | SERCOM3/PAD[0] | TCC2/WO[0] | TCC0/WO[6] |  | GCLK_IO[2]
PA17 | VDDIO | EXTINT[1] |  |  |  | X[5] |  | SERCOM1/PAD[1] | SERCOM3/PAD[1] | TCC2/WO[1] | TCC0/WO[7] |  | GCLK_IO[3]
PA18 | VDDIO | EXTINT[2] |  |  |  | X[6] |  | SERCOM1/PAD[2] | SERCOM3/PAD[2] | TC3/WO[0] | TCC0/WO[2] |  | AC/CMP[0]
PA19 | VDDIO | EXTINT[3] |  |  |  | X[7] |  | SERCOM1/PAD[3] | SERCOM3/PAD[3] | TC3/WO[1] | TCC0/WO[3] | I2S/SD[0] | AC/CMP[1]
PA20 | VDDIO | EXTINT[4] |  |  |  | X[8] |  | SERCOM5/PAD[2] | SERCOM3/PAD[2] | TC7/WO[0] | TCC0/WO[6] | I2S/SCK[0] | GCLK_IO[4]
PA21 | VDDIO | EXTINT[5] |  |  |  | X[9] |  | SERCOM5/PAD[3] | SERCOM3/PAD[3] | TC7/WO[1] | TCC0/WO[7] | I2S/FS[0] | GCLK_IO[5]
PA22 | VDDIO | EXTINT[6] |  |  |  | X[10] |  | SERCOM3/PAD[0] | SERCOM5/PAD[0] | TC4/WO[0] | TCC0/WO[4] |  | GCLK_IO[6]
PA23 | VDDIO | EXTINT[7] |  |  |  | X[11] |  | SERCOM3/PAD[1] | SERCOM5/PAD[1] | TC4/WO[1] | TCC0/WO[5] | USB/SOF 1kHz | GCLK_IO[7]
PA24 | VDDIO | EXTINT[12] |  |  |  |  |  | SERCOM3/PAD[2] | SERCOM5/PAD[2] | TC5/WO[0] | TCC1/WO[2] | USB/DM | 
PA25 | VDDIO | EXTINT[13] |  |  |  |  |  | SERCOM3/PAD[3] | SERCOM5/PAD[3] | TC5/WO[1] | TCC1/WO[3] | USB/DP | 
PA27 | VDDIO | EXTINT[15] |  |  |  |  |  |  |  |  |  |  | GCLK_IO[0]
PA28 | VDDIO | EXTINT[8] |  |  |  |  |  |  |  |  |  |  | GCLK_IO[0]
PA30 | VDDIO | EXTINT[10] |  |  |  |  |  |  | SERCOM1/PAD[2] | TCC1/WO[0] |  | SWCLK | GCLK_IO[0]
PA31 | VDDIO | EXTINT[11] |  |  |  |  |  |  | SERCOM1/PAD[3] | TCC1/WO[1] |  | SWDIO(4) | 
PB00 | VDDANA | EXTINT[0] |  | AIN[8] |  | Y[6] |  |  | SERCOM5/PAD[2] | TC7/WO[0] |  |  | 
PB01 | VDDANA | EXTINT[1] |  | AIN[9] |  | Y[7] |  |  | SERCOM5/PAD[3] | TC7/WO[1] |  |  | 
PB02 | VDDANA | EXTINT[2] |  | AIN[10] |  | Y[8] |  |  | SERCOM5/PAD[0] | TC6/WO[0] |  |  | 
PB03 | VDDANA | EXTINT[3] |  | AIN[11] |  | Y[9] |  |  | SERCOM5/PAD[1] | TC6/WO[1] |  |  | 
PB04 | VDDANA | EXTINT[4] |  | AIN[12] |  | Y[10] |  |  |  |  |  |  | 
PB05 | VDDANA | EXTINT[5] |  | AIN[13] |  | Y[11] |  |  |  |  |  |  | 
PB06 | VDDANA | EXTINT[6] |  | AIN[14] |  | Y[12] |  |  |  |  |  |  | 
PB07 | VDDANA | EXTINT[7] |  | AIN[15] |  | Y[13] |  |  |  |  |  |  | 
PB08 | VDDANA | EXTINT[8] |  | AIN[2] |  | Y[14] |  |  | SERCOM4/PAD[0] | TC4/WO[0] |  |  | 
PB09 | VDDANA | EXTINT[9] |  | AIN[3] |  | Y[15] |  |  | SERCOM4/PAD[1] | TC4/WO[1] |  |  | 
PB10 | VDDIO | EXTINT[10] |  |  |  |  |  |  | SERCOM4/PAD[2] | TC5/WO[0] | TCC0/WO[4] | I2S/MCK[1] | GCLK_IO[4]
PB11 | VDDIO | EXTINT[11] |  |  |  |  |  |  | SERCOM4/PAD[3] | TC5/WO[1] | TCC0/WO[5] | I2S/SCK[1] | GCLK_IO[5]
PB12 | VDDIO | EXTINT[12] |  |  |  | X[12] |  | SERCOM4/PAD[0] |  | TC4/WO[0] | TCC0/WO[6] | I2S/FS[1] | GCLK_IO[6]
PB13 | VDDIO | EXTINT[13] |  |  |  | X[13] |  | SERCOM4/PAD[1] |  | TC4/WO[1] | TCC0/WO[7] |  | GCLK_IO[7]
PB14 | VDDIO | EXTINT[14] |  |  |  | X[14] |  | SERCOM4/PAD[2] |  | TC5/WO[0] |  |  | GCLK_IO[0]
PB15 | VDDIO | EXTINT[15] |  |  |  | X[15] |  | SERCOM4/PAD[3] |  | TC5/WO[1] |  |  | GCLK_IO[1]
PB16 | VDDIO | EXTINT[0] |  |  |  |  |  | SERCOM5/PAD[0] |  | TC6/WO[0] | TCC0/WO[4] | I2S/SD[1] | GCLK_IO[2]
PB17 | VDDIO | EXTINT[1] |  |  |  |  |  | SERCOM5/PAD[1] |  | TC6/WO[1] | TCC0/WO[5] | I2S/MCK[0] | GCLK_IO[3]
PB22 | VDDIO | EXTINT[6] |  |  |  |  |  |  | SERCOM5/PAD[2] | TC7/WO[0] |  |  | GCLK_IO[0]
PB23 | VDDIO | EXTINT[7] |  |  |  |  |  |  | SERCOM5/PAD[3] | TC7/WO[1] |  |  | GCLK_IO[1]
PB30 | VDDIO | EXTINT[14] |  |  |  |  |  |  | SERCOM5/PAD[0] | TCC0/WO[0] | TCC1/WO[2] |  | 

## Slide 38: PMUX register options