## Slide 1: Chapter 7
ADC, DAC, and Sensor Interfacing

## Slide 2: Microcontroller Connection to Sensor via ADC

## Slide 3: An 8-bit ADC Block Diagram

## Slide 4: Resolution versus Step Size for ADC (Vref = 5V)
n-bit | Number of steps | Step size
8 | 256 | 5V /256 = 19.53 mV
10 | 1024 | 5V /1024 = 4.88 mV
12 | 4096 | 5V /4096 = 1.2 mV
16 | 65,536 | 5V /65,536 = 0.076 mV
Note: Vref = 5V |  | 

## Slide 5: Vref Relation to Vin Range for an 8-bit ADC
Vref (V) | Vin in Range (V) | Step Size (mV)
5.00 | 0 to 5 | 5 / 256 = 19.53
4.00 | 0 to 4 | 4 / 256 = 15.62
3.00 | 0 to 3 | 3 / 256 = 11.71
2.56 | 0 to 2.56 | 2.56 / 256 = 10
2.00 | 0 to 2 | 2 / 256 = 7.81
1.28 | 0 to 1.28 | 1.28 / 256 = 5
1.00 | 0 to 1 | 1 / 256 = 3.90
Note: In an 8-bit ADC, step size is Vref/256 |  | 

## Slide 6: Vref Relation to Vin Range for an 10-bit ADC
Vref (V) | VinRange (V) | Step Size (mV)
5.00 | 0 to 5 | 5 / 1024 = 4.88
4.96 | 0 to 4.096 | 4.096 / 1024 = 4
3.00 | 0 to 3 | 3 / 1024 = 2.93
2.56 | 0 to 2.56 | 2.56 / 1024 = 2.5
2.00 | 0 to 2 | 2 / 1024 = 2
1.28 | 0 to 1.28 | 1.28 / 1024 = 1.25
1.024 | 0 to 1.024 | 1.024 / 1024 = 1
Note: In a 10-bit ADC, step size is Vref/1024 |  | 

## Slide 7: A Simultaneous 2-bit ADC

## Slide 8: ADC0848 Parallel ADC Block Diagram

## Slide 9: MAX1112 Serial ADC Block Diagram

## Slide 10: Successive Approximation ADC

## Slide 11: Simplified Block Diagram of ADC in SAMD2x chip

## Slide 12: Some of the SAMD2x ADC Registers
Offset Address | Register
0x00 | CTRLA
0x01 | REFCTRL
0x03 | SAMPCTRL
0x04 | CTRLB
0x0C | SWTRIG
0x10 | INPUTCTRL
0x18 | INTGLAG
0x1A | RESULT
0x24 | GAINCORR
0x26 | OFFSETCORR
0x2A | DBGCTRL

## Slide 13: ADC Prescaler

## Slide 14: ADC Prescaler Options
PRESCALER | Description
0x0 | Divided by 4
0x1 | Divided by 8
0x2 | Divided by 16
0x3 | Divided by 32
0x4 | Divided by 64
0x5 | Divided by 128
0x6 | Divided by 256
0x7 | Divided by 512

## Slide 15: Sampling Time Control register

## Slide 16: Control B (CTRLB) Register

## Slide 17: ADC bit Resolution
RESSEL | Description
0x0 | 12-bit result
0x1 | For averaging
0x2 | 10-bit result
0x3 | 8-bit result

## Slide 18: PINMUXEN Register

## Slide 19: PINCFGn Register

## Slide 20: INPUTCTRL

## Slide 21: Analog input pin assignment in SAMD2x
I/O Pin | ADC | VREF | I/O Pin | ADC
PA02 | AIN[0] |  | PB02 | AIN[10]
PA03 | AIN[1] | VREFA | PB03 | AIN[11]
PB08 | AIN[2] |  | PB04 | AIN[12]
PB09 | AIN[3] |  | PB05 | AIN[13]
PA04 | AIN[4] | VREFB | PB06 | AIN[14]
PA05 | AIN[5] |  | PB07 | AIN[15]
PA06 | AIN[6] |  | PA08 | AIN[16]
PA07 | AIN[7] |  | PA09 | AIN[17]
PB00 | AIN[8] |  | PA10 | AIN[18]
PB01 | AIN[9] |  | PA11 | AIN[19]

## Slide 22: RESULT register holds conversion result

## Slide 23: RESULT Register for Right and Left Justified

## Slide 24: CTRLA (ADC Control A) register

## Slide 25: CTRLA Register of SAMD2x
Bit | Field | Descriptions
2 | RUNSTDBY | Run in Standby 0: The ADC is halted during standby sleep mode. 1: The ADC continues normal operation during standby sleep mode.
1 | ENABLE | Enable 0: The ADC is disabled. 1: The ADC is enabled.
0 | SWRST | Software Reset 0: There is no reset operation ongoing. 1: The reset operation is ongoing.

## Slide 26: INTFLG (Interrupt and Status Flag) Register for End-of-Conversion

## Slide 27: INTFLG Register Bits
Bit | Field | Descriptions
7-4 | Reserved | Reserved
3 | SYNCRDY | Synchronization Ready Writing a zero to this bit has no effect. Writing a one to this bit clears the Synchronization Ready interrupt flag.
2 | WINMON | Window Monitor Writing a zero to this bit has no effect. Writing a one to this bit clears the Window Monitor interrupt flag.
1 | OVERRUN | Overrun Writing a zero to this bit has no effect. Writing a one to this bit clears the Overrun interrupt flag.
0 | RESRDY | Result Ready Writing a zero to this bit has no effect. Writing a one to this bit clears the Result Ready interrupt flag.

## Slide 28: Reference Control register (REFCTRL)

## Slide 29: Reference Voltage Selection for Reference Control Register

## Slide 30: ADC Connection for Program 7-1

## Slide 31: Voltage References System (VREF) Control VREF register

## Slide 32: Voltage References System (VREF) Control Bit Definition
Bit | Field | Descriptions
1 | TSEN | Temperature Sensor Enable 0: Temperature sensor is disabled. 1: Temperature sensor is enabled and routed to an ADC input channel.
2 | BGOUTEN | Bandgap Output Enable 0: The bandgap output is not available as an ADC input channel. 1: The bandgap output is routed to an ADC input channel.

## Slide 33: Average Control Register (AVGCTRL)

## Slide 34: Accumulation Options for Multiple Consecutive Conversions
Number of Samples | SAMPLENUM | Intermediate Precision | Right Shift | Final Precision | Division Factor
1 | 0x0 | 12 bits | 0 | 12 bits | 1
2 | 0x1 | 13 bits | 0 | 13 bits | 1
4 | 0x2 | 14 bits | 0 | 14 bits | 1
8 | 0x3 | 15 bits | 0 | 15 bits | 1
16 | 0x4 | 16 bits | 0 | 16 bits | 1
32 | 0x5 | 17 bits | 1 | 16 bits | 2
64 | 0x6 | 18 bits | 2 | 16 bits | 4
128 | 0x7 | 19 bits | 3 | 16 bits | 8
256 | 0x8 | 20 bits | 4 | 16 bits | 16
512 | 0x9 | 21 bits | 5 | 16 bits | 32
1024 | 0xA | 22 bits | 6 | 16 bits | 64

## Slide 35: Averaging Options for Multiple Consecutive Conversions
Number of Samples | SAMPLENUM | ADJRES | Total Right Shift | Final Precision
1 | 0x0 | 0x0 | 0 | 12 bits
2 | 0x1 | 0x1 | 1 | 12 bits
4 | 0x2 | 0x2 | 2 | 12 bits
8 | 0x3 | 0x3 | 3 | 12 bits
16 | 0x4 | 0x4 | 4 | 12 bits
32 | 0x5 | 0x4 | 5 | 12 bits
64 | 0x6 | 0x4 | 6 | 12 bits
128 | 0x7 | 0x4 | 7 | 12 bits
256 | 0x8 | 0x4 | 8 | 12 bits
512 | 0x9 | 0x4 | 9 | 12 bits
1024 | 0xA | 0x4 | 10 | 12 bits

## Slide 36: Thermistor Resistance vs. Temperature
Temperature ('C) | Tf (K ohms)
0 | 29.490
25 | 10.000
50 | 3.893
75 | 1.700
100 | 0.817

## Slide 37: Thermistor (Copied from http://www.maximintegrated.com)

## Slide 38: LM34 and LM35

## Slide 39: Getting Data to the CPU

## Slide 40: LM34/35 Connection to ARM and Its Pin Configuration

## Slide 41: DAC Block Diagram

## Slide 42: Microcontroller Connection to DAC0808

## Slide 43: Atmel SADM2x DAC Block Diagram

## Slide 44: Control B Register (CTRLB)

## Slide 45: DAC Data Register

## Slide 46: Control A Register (CTRLA)

## Slide 47: Saw Tooth WaveForm

## Slide 48: Angle vs. Voltage Magnitude for Sine Wave

## Slide 49: Angle vs. Voltage Magnitude for Sine Wave