## Slide 1: Chapter 8
SPI Protocol and DAC Interfacing

## Slide 2: SPI Bus vs. Traditional Parallel Bus Connection to Microcontroller

## Slide 3: SPI Architecture

## Slide 4: Master SPI Connection to multiple slaves SPI in Parallel

## Slide 5: Master SPI Connection to multiple slaves SPI in serial

## Slide 6: SPI Clock Polarity and phase Mode 0 (CPOL = 0, CPHA = 0) and Mode 2 (CPOL = 1, CPHA = 0)

## Slide 7: SPI Clock Polarity and phase Mode 1 (CPOL = 0, CPHA = 1) and Mode 3 (CPOL = 1, CPHA = 1)

## Slide 8: SPI Clock Polarity and phase
Clock Polarity | Clock Phase | Data read and change time | SPI Mode
0 | 0 | read on rising edge, changed on a falling edge | 0
0 | 1 | read on falling edge, changed on a rising edge | 1
1 | 0 | read on falling edge, changed on a rising edge | 2
1 | 1 | read on rising edge, changed on a falling edge | 3

## Slide 9: SAMD2x SPI Module Base Addresses
SERCOM Module | Base Address
SERCOM0 | 0x42000800
SERCOM1 | 0x42000C00
SERCOM2 | 0x42001000
SERCOM3 | 0x42001400
SERCOM4 | 0x42001800
SERCOM5 | 0x42001C00

## Slide 10: SAMD2x SPI Registers
Register Name | Register Function | Register Address Offset (Hex)
CTRLA | Control A | 0x00
CTRLB | Control B | 0x04
BAUD | Baud rate | 0x0C
INTENCLR | Interrupt Enable Clear | 0x14
INTENSET | Interrupt Enable Set | 0x16
INTFLAG | Interrupt Flag | 0x18
STATUS | Status | 0x1A
SYNCBUSY | Synchronization Busy | 0x1D
ADDR | Address | 0x24
DATA | Receive and Transmit buffer | 0x28
DBGCTRL | Debug Control | 0x30

## Slide 11: SPI Control A (CTRLA) Register in SAMD2x

## Slide 12: CTRLA (Control A) Register
Bits | Name | Function | Description
30 | DORD | Data Order | 0: MSB is transferred first. 1: LSB is transferred first.
29 | CPOL | Clock Polarity | 0: SCK is low when idle. The leading edge of a clock cycle is a rising edge, while the trailing edge is a falling edge. 1: SCK is high when idle. The leading edge of a clock cycle is a falling edge, while the trailing edge is a rising edge.
28 | CPHA | Clock Phase | 0: The data is sampled on a leading SCK edge and changed on a trailing SCK edge. 1: The data is sampled on a trailing SCK edge and changed on a leading SCK edge.
27-24 | FORM[3:0] | Frame Format | 
21-20 | DIPO[1:0] | Data In Pinout | In master operation, DO is MOSI. In slave operation, DO is MISO.
8 | IBON | Immediate Buffer Overflow Notification | 0: STATUS.BUFOVF is asserted when it occurs in the data stream. 1: STATUS.BUFOVF is asserted immediately upon buffer overflow.
7 | RUNSTDBY | Run In Standby | This bit defines the functionality in standby sleep mode.
4-2 | MODE | Operating Mode | 0x2: SPI slave operation 0x3: SPI master operation For UART and I2C options, see relevant chapters
1 | ENABLE | Enable | 0: The peripheral is disabled or being disabled. 1: The peripheral is enabled or being enabled.
0 | SWRST | Software Reset | 0: There is no reset operation ongoing. 1: The reset operation is ongoing.

## Slide 13: SPI Control B (CTRLB) Registers in SAMD2x

## Slide 14: Using SAMD2x SPI module as Master

## Slide 15: BAUD Register SPI Baud Rate

## Slide 16: DATA register

## Slide 17: Interrupt Flag (INTFLAG) Register

## Slide 18: Interrupt Flag Register Bits
Bits | Name | Function | Description
0 | DRE | Data Register Empty | The bit is 1 when the transmit DATA is empty and can accept another byte of data.
1 | TXC | Transmit Complete | The bit is 1 when both transmit DATA is empty and the shift register is empty. It is cleared by writing a 1 to it.
2 | RXC | Receive Complete | The bit is 1 when there is new data in the receive buffer registers. It is cleared when data are read.

## Slide 19: PINCFGn register (notice the PMUXEN bit)

## Slide 20: PMUX register for choosing peripheral functions

## Slide 21: PORT pin Function multiplexing options

## Slide 22: PORT pin Function multiplexing
 |  | A (0) | B (1) |  |  |  |  | C (2) | D (3) | E (4) | F (5) | G (6) | H (7)
I/O Pin | Supply | EIC | REF | ADC | AC | PTC | DAC | SERCOM | SERCOM-ALT | TC/TCC | TCC | COM | AC/GCLK
PA00 | VDDANA | EXTINT[0] |  |  |  |  |  |  | SERCOM1/PAD[0] | TCC2/WO[0] |  |  | 
PA01 | VDDANA | EXTINT[1] |  |  |  |  |  |  | SERCOM1/PAD[1] | TCC2/WO[1] |  |  | 
PA02 | VDDANA | EXTINT[2] |  | AIN[0] |  | Y[0] | VOUT |  |  |  |  |  | 
PA03 | VDDANA | EXTINT[3] | ADC/VREFA DAC/VREFA | AIN[1] |  | Y[1] |  |  |  |  |  |  | 
PA04 | VDDANA | EXTINT[4] | ADC/VREFB | AIN[4] | AIN[0] | Y[2] |  |  | SERCOM0/PAD[0] | TCC0/WO[0] |  |  | 
PA05 | VDDANA | EXTINT[5] |  | AIN[5] | AIN[1] | Y[3] |  |  | SERCOM0/PAD[1] | TCC0/WO[1] |  |  | 
PA06 | VDDANA | EXTINT[6] |  | AIN[6] | AIN[2] | Y[4] |  |  | SERCOM0/PAD[2] | TCC1/WO[0] |  |  | 
PA07 | VDDANA | EXTINT[7] |  | AIN[7] | AIN[3] | Y[5] |  |  | SERCOM0/PAD[3] | TCC1/WO[1] |  | I2S/SD[0] | 
PA08 | VDDIO | NMI |  | AIN[16] |  | X[0] |  | SERCOM0/PAD[0] | SERCOM2/PAD[0] | TCC0/WO[0] | TCC1/WO[2] | I2S/SD[1] | 
PA09 | VDDIO | EXTINT[9] |  | AIN[17] |  | X[1] |  | SERCOM0/PAD[1] | SERCOM2/PAD[1] | TCC0/WO[1] | TCC1/WO[3] | I2S/MCK[0] | 
PA10 | VDDIO | EXTINT[10] |  | AIN[18] |  | X[2] |  | SERCOM0/PAD[2] | SERCOM2/PAD[2] | TCC1/WO[0] | TCC0/WO[2] | I2S/SCK[0] | GCLK_IO[4]
PA11 | VDDIO | EXTINT[11] |  | AIN[19] |  | X[3] |  | SERCOM0/PAD[3] | SERCOM2/PAD[3] | TCC1/WO[1] | TCC0/WO[3] | I2S/FS[0] | GCLK_IO[5]
PA12 | VDDIO | EXTINT[12] |  |  |  |  |  | SERCOM2/PAD[0] | SERCOM4/PAD[0] | TCC2/WO[0] | TCC0/WO[6] |  | AC/CMP[0]
PA13 | VDDIO | EXTINT[13] |  |  |  |  |  | SERCOM2/PAD[1] | SERCOM4/PAD[1] | TCC2/WO[1] | TCC0/WO[7] |  | AC/CMP[1]
PA14 | VDDIO | EXTINT[14] |  |  |  |  |  | SERCOM2/PAD[2] | SERCOM4/PAD[2] | TC3/WO[0] | TCC0/WO[4] |  | GCLK_IO[0]
PA15 | VDDIO | EXTINT[15] |  |  |  |  |  | SERCOM2/PAD[3] | SERCOM4/PAD[3] | TC3/WO[1] | TCC0/WO[5] |  | GCLK_IO[1]
PA16 | VDDIO | EXTINT[0] |  |  |  | X[4] |  | SERCOM1/PAD[0] | SERCOM3/PAD[0] | TCC2/WO[0] | TCC0/WO[6] |  | GCLK_IO[2]
PA17 | VDDIO | EXTINT[1] |  |  |  | X[5] |  | SERCOM1/PAD[1] | SERCOM3/PAD[1] | TCC2/WO[1] | TCC0/WO[7] |  | GCLK_IO[3]
PA18 | VDDIO | EXTINT[2] |  |  |  | X[6] |  | SERCOM1/PAD[2] | SERCOM3/PAD[2] | TC3/WO[0] | TCC0/WO[2] |  | AC/CMP[0]
PA19 | VDDIO | EXTINT[3] |  |  |  | X[7] |  | SERCOM1/PAD[3] | SERCOM3/PAD[3] | TC3/WO[1] | TCC0/WO[3] | I2S/SD[0] | AC/CMP[1]
PA20 | VDDIO | EXTINT[4] |  |  |  | X[8] |  | SERCOM5/PAD[2] | SERCOM3/PAD[2] | TC7/WO[0] | TCC0/WO[6] | I2S/SCK[0] | GCLK_IO[4]
PA21 | VDDIO | EXTINT[5] |  |  |  | X[9] |  | SERCOM5/PAD[3] | SERCOM3/PAD[3] | TC7/WO[1] | TCC0/WO[7] | I2S/FS[0] | GCLK_IO[5]
PA22 | VDDIO | EXTINT[6] |  |  |  | X[10] |  | SERCOM3/PAD[0] | SERCOM5/PAD[0] | TC4/WO[0] | TCC0/WO[4] |  | GCLK_IO[6]
PA23 | VDDIO | EXTINT[7] |  |  |  | X[11] |  | SERCOM3/PAD[1] | SERCOM5/PAD[1] | TC4/WO[1] | TCC0/WO[5] | USB/SOF 1kHz | GCLK_IO[7]
PA24 | VDDIO | EXTINT[12] |  |  |  |  |  | SERCOM3/PAD[2] | SERCOM5/PAD[2] | TC5/WO[0] | TCC1/WO[2] | USB/DM | 
PA25 | VDDIO | EXTINT[13] |  |  |  |  |  | SERCOM3/PAD[3] | SERCOM5/PAD[3] | TC5/WO[1] | TCC1/WO[3] | USB/DP | 
PA27 | VDDIO | EXTINT[15] |  |  |  |  |  |  |  |  |  |  | GCLK_IO[0]
PA28 | VDDIO | EXTINT[8] |  |  |  |  |  |  |  |  |  |  | GCLK_IO[0]
PA30 | VDDIO | EXTINT[10] |  |  |  |  |  |  | SERCOM1/PAD[2] | TCC1/WO[0] |  | SWCLK | GCLK_IO[0]
PA31 | VDDIO | EXTINT[11] |  |  |  |  |  |  | SERCOM1/PAD[3] | TCC1/WO[1] |  | SWDIO(4) | 
PB00 | VDDANA | EXTINT[0] |  | AIN[8] |  | Y[6] |  |  | SERCOM5/PAD[2] | TC7/WO[0] |  |  | 
PB01 | VDDANA | EXTINT[1] |  | AIN[9] |  | Y[7] |  |  | SERCOM5/PAD[3] | TC7/WO[1] |  |  | 
PB02 | VDDANA | EXTINT[2] |  | AIN[10] |  | Y[8] |  |  | SERCOM5/PAD[0] | TC6/WO[0] |  |  | 
PB03 | VDDANA | EXTINT[3] |  | AIN[11] |  | Y[9] |  |  | SERCOM5/PAD[1] | TC6/WO[1] |  |  | 
PB04 | VDDANA | EXTINT[4] |  | AIN[12] |  | Y[10] |  |  |  |  |  |  | 
PB05 | VDDANA | EXTINT[5] |  | AIN[13] |  | Y[11] |  |  |  |  |  |  | 
PB06 | VDDANA | EXTINT[6] |  | AIN[14] |  | Y[12] |  |  |  |  |  |  | 
PB07 | VDDANA | EXTINT[7] |  | AIN[15] |  | Y[13] |  |  |  |  |  |  | 
PB08 | VDDANA | EXTINT[8] |  | AIN[2] |  | Y[14] |  |  | SERCOM4/PAD[0] | TC4/WO[0] |  |  | 
PB09 | VDDANA | EXTINT[9] |  | AIN[3] |  | Y[15] |  |  | SERCOM4/PAD[1] | TC4/WO[1] |  |  | 
PB10 | VDDIO | EXTINT[10] |  |  |  |  |  |  | SERCOM4/PAD[2] | TC5/WO[0] | TCC0/WO[4] | I2S/MCK[1] | GCLK_IO[4]
PB11 | VDDIO | EXTINT[11] |  |  |  |  |  |  | SERCOM4/PAD[3] | TC5/WO[1] | TCC0/WO[5] | I2S/SCK[1] | GCLK_IO[5]
PB12 | VDDIO | EXTINT[12] |  |  |  | X[12] |  | SERCOM4/PAD[0] |  | TC4/WO[0] | TCC0/WO[6] | I2S/FS[1] | GCLK_IO[6]
PB13 | VDDIO | EXTINT[13] |  |  |  | X[13] |  | SERCOM4/PAD[1] |  | TC4/WO[1] | TCC0/WO[7] |  | GCLK_IO[7]
PB14 | VDDIO | EXTINT[14] |  |  |  | X[14] |  | SERCOM4/PAD[2] |  | TC5/WO[0] |  |  | GCLK_IO[0]
PB15 | VDDIO | EXTINT[15] |  |  |  | X[15] |  | SERCOM4/PAD[3] |  | TC5/WO[1] |  |  | GCLK_IO[1]
PB16 | VDDIO | EXTINT[0] |  |  |  |  |  | SERCOM5/PAD[0] |  | TC6/WO[0] | TCC0/WO[4] | I2S/SD[1] | GCLK_IO[2]
PB17 | VDDIO | EXTINT[1] |  |  |  |  |  | SERCOM5/PAD[1] |  | TC6/WO[1] | TCC0/WO[5] | I2S/MCK[0] | GCLK_IO[3]
PB22 | VDDIO | EXTINT[6] |  |  |  |  |  |  | SERCOM5/PAD[2] | TC7/WO[0] |  |  | GCLK_IO[0]
PB23 | VDDIO | EXTINT[7] |  |  |  |  |  |  | SERCOM5/PAD[3] | TC7/WO[1] |  |  | GCLK_IO[1]
PB30 | VDDIO | EXTINT[14] |  |  |  |  |  |  | SERCOM5/PAD[0] | TCC0/WO[0] | TCC1/WO[2] |  | 

## Slide 23: LTC1661 Internal Block Diagram

## Slide 24: Sending a Packet of Data to LTC166x

## Slide 25: LTC1661 DAC Control Functions
A3 A2 A1 A0 | Interrupt Register | DAC Register | Power Down Status | Comments
0 0 0 0 | No Change | No Update | No Change | No operation. power-down status unchanged
0 0 0 1 | Load DAC A | No Update | No Change | Load input register A with data. DAC outputs unchanged. power-down Status unchanged
0 0 1 0 | Load DAC B | No Update | No Change | Load input register B with data. DAC outputs unchanged. power-down status unchanged
0 0 1 1 | - | - | - | Reserved
0 1 0 0 | - | - | - | Reserved
0 1 0 1 | - | - | - | Reserved
0 1 1 0 | - | - | - | Reserved
0 1 1 1 | - | - | - | Reserved
1 0 0 0 | No Change | Update Outputs | Wake | Load both DAC Regs with existing contents of input Regs. Outputs update. Part wakes up
1 0 0 1 | Load DAC A | Update Outputs | Wake | Load input Reg A. Load DAC Regs with new contents of input Reg A and existing contents of Reg B. Outputs update.
1 0 1 0 | Load DAC B | Update Outputs | Wake | Load input Reg B. Load DAC Regs with existing contentsof input Reg A and new contents of Reg B. Outputs update
1 0 1 1 | - | - | - | Reserved
1 1 0 0 | - | - | - | Reserved
1 1 0 1 | No Change | No Update | Wake | Part wakes up. Input and DAC Regs unchanged. DAC outputs reflect existing contents of DAC Regs
1 1 1 0 | No Change | No Update | Sleep | Part goes to sleep. Input and DAC Regs unchanged. DAC outputs set to high impedance state
1 1 1 1 | Load ADCs A, B with same 10-bit code | Update Outputs | Wake | Load both input Regs. Load both DAC Regs with new contents of input Regs. Outputs update. Part wakes up

## Slide 26: Connecting LTC1661 to the SAMD21

## Slide 27: The Generated Sawtooth waveform