## Slide 1: Chapter 2
Freescale ARM I/O Programming

## Slide 2: Freescale KL25Z128VLK4 Microcontroller High-Level Block Diagram

## Slide 3: Freescale FRDM Trainer board

## Slide 4: Memory Map

## Slide 5: Memory Map in KL25Z128VLK4
 | Allocated size | Allocated address
Flash | 128KB | 0x00000000 to 0x0001FFFF
SRAM | 16KB | 0x1FFFF000 to 0x20002FFF
I/O | All the peripherals | 0x400FF000 to 0x400FFFFF

## Slide 6: GPIO Memory Map

## Slide 7: Fields Values Description
Field | Description | Some Valid Values
Q | Qualification status | • M = Fully qualified, general market flow • P = Prequalification
KL## | Kinetis family | • KL25
A | Key attribute | • Z = Cortex-M0+
FFF | Program Flash memory size | • 32 = 32 KB • 64 = 64 KB • 128 = 128 KB
T | Temperature range (°C) | • V = –40 to 105
PP | Package identifier | • FM = 32 QFN (5 mm x 5 mm) • FT = 48 QFN (7 mm x 7 mm) • LH = 64 LQFP (10 mm x 10 mm) • LK = 80 LQFP (12 mm x 12 mm)
CC | Maximum CPU frequency (MHz) | • 4 = 48 MHz

## Slide 8: Kinetis MCU Portfolio

## Slide 9: KL25Z128VLK4 Pin-out

## Slide 10: The Data and Direction Registers and a Simplified View of an I/O pin

## Slide 11: GPIOx_PDOR (Port Data Output Register)

## Slide 12: GPIOx_PDDR (Port Data Direction Register)

## Slide 13: Some GPIO Registers for PORTA
Address | Name | Description | Type | Reset Value
0x400F F000 | GPIOA_PDOR | Port Data Output Register | R/W | 0x00000000
0x400F F004 | GPIOA_PSOR | Port Set Output register | W (always reads 0) | 0x00000000
0x400F F008 | GPIOA_PCOR | Port Clear Output Register | W (always reads 0) | 0x00000000
0x400F F00C | GPIOA_PTOR | Port Toggle Output Register | W (always reads 0) | 0x00000000
0x400F F010 | GPIOA_PDIR | Port Data Input Register | R | 0x00000000
0x400F F014 | GPIOA_PDDR | Port Data Direction Register | R/W | 0x00000000

## Slide 14: Alternative Functions of Pins

## Slide 15: PORTx_PCRn Register is used to select alternate pin functions (from Sec 11.5 of KL25 Ref. Man.)

## Slide 16: SIM_SCGC5 (System Clock Gating Control Register 5) Register

## Slide 17: LED connection to PTB and PTD Freescale FRDM board

## Slide 18: PSOR (Port Set Output Register)

## Slide 19: PCOR (Port Clear Output Register)

## Slide 20: PTOR (Port Toggle Output Register)

## Slide 21: Clock setup modes in Keil MDK-ARM v5 Freescale Kinetis KLxx Series Device Family Support Pack
CLOCK_SETUP | Mode | Reference clock source | Core clock | Bus clock
0 | FLL Engaged Internal | slow internal clock 32.768kHz | 41.94MHz | 13.98MHz
1 | PLL Engaged External | external crystal 8MHz | 48MHz | 24MHz
2 | Bypassed Low Power External | external crystal 8MHz | 8MHz | 8MHz

## Slide 22: Connecting External Switches to the Microcontroller

## Slide 23: PS and PE bits

## Slide 24: Seven-Segment

## Slide 25: Assignments of port pins to each segments of a 7-seg LED
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
. | g | f | e | d | c | b | a

## Slide 26: Segment patterns for the 10 decimal digits for a common cathode 7-seg LED
Num | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | Hex value
 | . | g | f | e | d | c | b | a | 
0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0x3F
1 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0x06
2 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 0x5B
3 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 0x4F
4 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0x66
5 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 0x6D
6 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0x7D
7 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0x07
8 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0x7F
9 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0x6F

## Slide 27: Microcontroller Connection to 7-segment LED

## Slide 28: Microcontroller Connection to 7-segment LED with Buffer Driver