## Slide 1: Chapter 8
SPI Protocol and DAC Interfacing

## Slide 2: SPI Bus vs. Traditional Parallel Bus Connection to Microcontroller

## Slide 3: SPI Architecture

## Slide 4: Master SPI Connection to multiple slaves SPI in Parallel

## Slide 5: Master SPI Connection to multiple slaves SPI in serial

## Slide 6: SPI Clock Polarity and phase Mode 0 (CPOL = 0, CPHA = 0) and Mode 2 (CPOL = 1, CPHA = 0)

## Slide 7: SPI Clock Polarity and phase Mode 1 (CPOL = 0, CPHA = 1) and Mode 3 (CPOL = 1, CPHA = 1)

## Slide 8: SPI Clock Polarity and phase
Clock Polarity | Clock Phase | Data read and change time | SPI Mode
0 | 0 | read on rising edge, changed on a falling edge | 0
0 | 1 | read on falling edge, changed on a rising edge | 1
1 | 0 | read on falling edge, changed on a rising edge | 2
1 | 1 | read on rising edge, changed on a falling edge | 3

## Slide 9: STM32F4xx Arm SPI Module Base Addresses
SPI Module | Base Address
SPI1 | 0x4001 3000 - 0x4001 33FF
SPI2 | 0x4000 3800 - 0x4000 3BFF
SPI3 | 0x4000 3C00 - 0x4000 3FFF

## Slide 10: STM32F4xx SPI Registers
Register Name | Register Function | Register Address Offset
SPI_CR1 | Control 1 | 0x00
SPI_CR2 | Control 2 | 0x04
SPI_SR | Status | 0x08
SPI_DR | Data | 0x0C

## Slide 11: RCC APB1 peripheral clock enable register (RCC_APB1ENR)

## Slide 12: RCC APB2 peripheral clock enable register (RCC_APB2ENR)

## Slide 13: SPI Control 1 (SPI_CR1) Register in STM32F4xx

## Slide 14: SPI_CR2 (Contolr 2) Registers in STM32F4xx
Bit 7
TXEIE:
Tx buffer empty interrupt enable
0: TXE interrupt masked
1: TXE interrupt not masked. Used to generate an interrupt request when the TXE flag is
set.
Bit 6
RXNEIE:
RX buffer not empty interrupt enable
0: RXNE interrupt masked
1: RXNE interrupt not masked. Used to generate an interrupt request when the RXNE flag is set.
Bit 5
ERRIE:
Error interrupt enable
This bit controls the generation of an
interrupt when an error condition occurs (OVR,
CRCERR, MODF, FRE in SPI mode, and UDR, OVR, FRE in I
2
S mode).
0: Error interrupt is masked
1: Error interrupt is enabled
Bit 4
FRF
: Frame format
0: SPI Motorola mode
1: SPI TI mode

## Slide 15: Using STM32F4xx SPI module as Master

## Slide 16: Using STM32F4xx SPI module as Master

## Slide 17: SPI_DR (Data) register

## Slide 18: SPI_SR (Status) Register

## Slide 19: SPI_SR (Status) Register
Bits | Name | Function | Description
1 | TXE: Transmit buffer empty | Data Register Empty | The bit is 1 when the transmit data is empty and can accept another byte of data.
0 | RXNE: Receive buffer not empty | Receive Complete | The bit is 1 when there is new data in the receive buffer registers. It is cleared when data are read.

## Slide 20: Alternate pin Function multiplexing for STM32F446RE (See Appendix B for complete list)

## Slide 21: GPIOx_MODER
Bits 2y:2y+1
MODERy[1:0]:
Port x
configuration bits (y = 0..15)
These bits are written by software to configure the I/O direction mode.
00: Input (reset state)
01: General purpose output mode
10: Alternate function mode
11: Analog mode

## Slide 22: GPIOx_AFRL Register
Bits 31:0 AFRLy: Alternate function selection for port x bit y (y = 0..7)
These bits are written by software to configure alternate function I/Os
AFRLy selection:
0000: AF0
0001: AF1
0010: AF2
0011: AF3
0100: AF4
0101: AF5
0110: AF6
0111: AF7
1000: AF8
1001: AF9
1010: AF10
1011: AF11
1100: AF12
1101: AF13
1110: AF14
1111: AF15

## Slide 23: LTC1661 Internal Block Diagram

## Slide 24: Sending a Packet of Data to LTC166x

## Slide 25: LTC1661 DAC Control Functions
A3 A2 A1 A0 | Interrupt Register | DAC Register | Power Down Status | Comments
0 0 0 0 | No Change | No Update | No Change | No operation. power-down status unchanged
0 0 0 1 | Load DAC A | No Update | No Change | Load input register A with data. DAC outputs unchanged. power-down Status unchanged
0 0 1 0 | Load DAC B | No Update | No Change | Load input register B with data. DAC outputs unchanged. power-down status unchanged
0 0 1 1 | - | - | - | Reserved
0 1 0 0 | - | - | - | Reserved
0 1 0 1 | - | - | - | Reserved

## Slide 26: LTC1661 DAC Control Functions (Cont.)
A3 A2 A1 A0 | Interrupt Register | DAC Register | Power Down Status | Comments
0 1 1 0 | - | - | - | Reserved
0 1 1 1 | - | - | - | Reserved
1 0 0 0 | No Change | Update Outputs | Wake | Load both DAC Regs with existing contents of input Regs. Outputs update. Part wakes up
1 0 0 1 | Load DAC A | Update Outputs | Wake | Load input Reg A. Load DAC Regs with new contents of input Reg A and existing contents of Reg B. Outputs update.
1 0 1 0 | Load DAC B | Update Outputs | Wake | Load input Reg B. Load DAC Regs with existing contentsof input Reg A and new contents of Reg B. Outputs update

## Slide 27: LTC1661 DAC Control Functions (Cont.)
A3 A2 A1 A0 | Interrupt Register | DAC Register | Power Down Status | Comments
1 0 1 1 | - | - | - | Reserved
1 1 0 0 | - | - | - | Reserved
1 1 0 1 | No Change | No Update | Wake | Part wakes up. Input and DAC Regs unchanged. DAC outputs reflect existing contents of DAC Regs
1 1 1 0 | No Change | No Update | Sleep | Part goes to sleep. Input and DAC Regs unchanged. DAC outputs set to high impedance state
1 1 1 1 | Load ADCs A, B with same 10-bit code | Update Outputs | Wake | Load both input Regs. Load both DAC Regs with new contents of input Regs. Outputs update. Part wakes up

## Slide 28: Connecting LTC1661 to the STM32F4xx

## Slide 29: The Generated sawTooth waveform