## Slide 1: Chapter 8
SPI Protocol and DAC Interfacing

## Slide 2: SPI Bus vs. Traditional Parallel Bus Connection to Microcontroller

## Slide 3: SPI Architecture

## Slide 4: SPI Clock Polarity and phase

## Slide 5: SPI Clock Polarity and phase
Clock Polarity | Clock Phase | Data read and change time | SPI Mode
0 | 0 | read on falling edge, changed on a rising edge | 0
0 | 1 | read on rising edge, changed on a falling edge | 1
1 | 0 | read on rising edge, changed on a falling edge | 2
1 | 1 | read on falling edge, changed on a rising edge | 3

## Slide 6: SSI Module Base Address
SSI Module | Base Address
SSI0 | 0x40008000
SSI1 | 0x40009000
SSI2 | 0x4000A000
SSI3 | 0x4000B000

## Slide 7: RCGCSSI, Offset 0x61C

## Slide 8: SSICR0, Offset 0

## Slide 9: eUSCI Registers
Bits | Name | Function | Description
0-3 | DSS | SSI Data Size Select | 0x03 to 0x0F for 4-bit to 16-bit data size 0x07 means 8-bit data size
4-5 | FRF | SSI Frame Format Select | 0 for SPI, 1 for TI, and 2 for MICROWIRE frame format
6 | SPO | SSI Serial Clock Polarity | Clock polarity
7 | SPH | SSI Serial Clock Phase | Clock phase
8-15 | SCR | SSI Serial Clock Rate | BR=SysClk/(CPSDVSR * (1 + SCR))

## Slide 10: Bit Rate selection

## Slide 11: Register 5, SSI Clock Prescale (SSICPSR), offset 0x010

## Slide 12: Register 2, SSI Control 1 (SSICR1), offset 0x004

## Slide 13: SSIDR register

## Slide 14: Register 3, SSI Data (SSIDR), offset 0x008

## Slide 15: Register 4, SSI Status (SSISR), offset 0x00C

## Slide 16: SSI Status (SSISR)
Bits | Name | Function | Description
0 | TFE | SSI Transmit FIFO Empty | The bit is 1 when the transmit FIFO is empty
1 | TNF | SSI Transmit FIFO Not Full | The bit is 1 when the SSI transmit FIFO not full
2 | RNE | SSI Receive FIFO Not Empty | The bit is 1 when the receive FIFO is not empty
3 | RFF | SSI Receive FIFO Full | The bit is 1 when the receive FIFO is full
4 | BSY | SSI Busy Bit | The bit is 1 when the SSI is currently transmitting or receiving

## Slide 17: GPIO Pin Assignment for all 4 SSI Modules
SSI Module Pin | GPIO Pin | SSI Module Pin | GPIO Pin
SSI0Clk | PA2 | SSI2Clk | PB4
SSI0Fss | PA3 | SSI2Fss | PB5
SSI0Rx | PA4 | SSI2Rx | PB6
SSI0Tx | PA5 | SSI2TX | PB7
SSI1Clk | PD0 or PF2 | SSI3Clk | PD0
SSI1Fss | PD1 or PF3 | SSI3Fss | PD1
SSI1Rx | PD2 or PF0 | SSI3Rx | PD2
SSI1TX | PD3 or PF1 | SSI3TX | PD3

## Slide 18: Register 6, SSIIM

## Slide 19: Register 6, SSIIM
Bits | Name | Function | Description
0 | RORIM | SSI Receive Overrun Interrupt Mask | The receive FIFO overrun interrupt is masked when RORIM is zero and not masked when it is one
1 | RTIM | SSI Receive Time-Out Interrupt Mask | The receive FIFO time-out interrupt is masked when RTIM is zero and not masked when it is one
2 | RXIM | SSI Receive FIFO Interrupt Mask | The receive FIFO interrupt is masked when RXIM is zero and not masked when it is one
3 | TXIM | SSI Transmit FIFO Interrupt Mask | The transmit FIFO interrupt is masked when TXIM is zero and not masked when it is one

## Slide 20: LTC1661 Internal Block Diagram

## Slide 21: Sending a Packet of Data to LTC166x

## Slide 22: LTC1661 DAC Control Functions
A3 A2 A1 A0 | Interrupt Register | DAC Register | Power Down Status | Comments
0 0 0 0 | No Change | No Update | No Change | No operation. power-down status unchanged
0 0 0 1 | Load DAC A | No Update | No Change | Load input register A with data. DAC outputs unchanged. power-down Status unchanged
0 0 1 0 | Load DAC B | No Update | No Change | Load input register B with data. DAC outputs unchanged. power-down status unchanged
0 0 1 1 | - | - | - | Reserved
0 1 0 0 | - | - | - | Reserved
0 1 0 1 | - | - | - | Reserved

## Slide 23: LTC1661 DAC Control Functions (Cont.)
A3 A2 A1 A0 | Interrupt Register | DAC Register | Power Down Status | Comments
0 1 1 0 | - | - | - | Reserved
0 1 1 1 | - | - | - | Reserved
1 0 0 0 | No Change | Update Outputs | Wake | Load both DAC Regs with existing contents of input Regs. Outputs update. Part wakes up
1 0 0 1 | Load DAC A | Update Outputs | Wake | Load input Reg A. Load DAC Regs with new contents of input Reg A and existing contents of Reg B. Outputs update.
1 0 1 0 | Load DAC B | Update Outputs | Wake | Load input Reg B. Load DAC Regs with existing contentsof input Reg A and new contents of Reg B. Outputs update

## Slide 24: LTC1661 DAC Control Functions (Cont.)
A3 A2 A1 A0 | Interrupt Register | DAC Register | Power Down Status | Comments
1 0 1 1 | - | - | - | Reserved
1 1 0 0 | - | - | - | Reserved
1 1 0 1 | No Change | No Update | Wake | Part wakes up. Input and DAC Regs unchanged. DAC outputs reflect existing contents of DAC Regs
1 1 1 0 | No Change | No Update | Sleep | Part goes to sleep. Input and DAC Regs unchanged. DAC outputs set to high impedance state
1 1 1 1 | Load ADCs A, B with same 10-bit code | Update Outputs | Wake | Load both input Regs. Load both DAC Regs with new contents of input Regs. Outputs update. Part wakes up

## Slide 25: Connecting LTC1661 to the Microcontroller

## Slide 26: The Generated sawTooth waveform